CB&Q DEPRESSED FLAT CAR FD-1 #91875

Number built:  1

Page:  F-12, Drawing #:  59395-0

Builder:  Havelock

Year built:  1958

Truck Number:  11

General Drawing:  61603

Trucks:  4 ea, 2 axle, 4 wheel

Floor Length:  16' 6.5", 30' 0", 16' 6.5"

Distance between truck centers:  53'0"

Capacity:  300M

Steel loading platform

Remarks:  'X' Loading Platform

Length loading platform:  30' 0"

Width loading platform:  10' 0"

Length end decks:  16' 6.5"

Width end decks:  8' 0"

Width of underframe:  8' 3.875"

Length over end sills:  72' 3"

Length over pulling face:  75' 4"

Length over strikers:  72' 10"

Height of end deck (at end sill):  4' 10.75"

Height of loading platform:  30"

Bottom of

Height of end deck:  5' 0.125"

Bottom of center deck above rails:  7.875"

Truck bolster center line to pulling face:  11'2"

Center line of truck bolster to center line of truck:  5' 0"

Truck wheel base:  5'0"