CB&Q FLAT CAR FM-17 #91899

Number built:  1

Page:   F-1, Drawing #: 59358 A

Builder:  Havelock

Year built:  1952

Truck #:  ?

Trucks:  2 ea, 3 axle, 6 wheel, 6.5"x12" Timken bearings

Spacing between axles: 4'6"

General Drawing:  91533

Total weight:  106,000 lbs

Capacity:  250M

No stake pockets

Cast underframe

Handbrake:  Union Rwy Equip Co (drop), both ends

Length over strikers:  54'0.25"

Length over flooring:  53'0"

Flooring:  3" wood

Width over flooring:  10'6"

Width over casting:  9'8.5"

Height over flooring:  3'9.75"

Truck centers:  35'0"

Truck centers to ends of car:  9'6.125"